## Slide 1
Candidate for the degree of Master of Science:
Eng. Ivan de Souza Rehder
Virtual reality for the human-centred design of assistive devices
Thesis Committee Composition:
Chairperson: Prof. Dr. Luís Gonzaga Trabasso (ITA)
Advisor: Profª. Drª. Emilia Villani (ITA)
Coadvisor: Prof. Dr. Edmar Thomaz da Silva (ITA)
Internal member: Prof. Dr. Christopher S. Cerqueira (ITA)
External member: Prof. Dr. Petter Krus(INPE)
August 4th, 2022

## Slide 2
Conclusion and outlook
5.
Results and discussion
4.
Materials and Methods
3.
Objectives and Approach
2.
Introduction
1.
Agenda

## Slide 3
Conclusion and outlook
5.
Results and discussion
4.
Materials and Methods
3.
Objectives and Approach
2.
Introduction
1.
Agenda

## Slide 4
Introduction: Motivations
2.2 billions some visual impairment.
  43,3 million are blind
  295 million have moderate or severe vision impairment.
Dissatisfaction of the community
COVID-19
  WHO recommendations

## Slide 5
Introduction: Human Factors
Performance shortfalls and failures
Engineering, psychology and physiology
Notes: • Studies in the area of Human Factors started during the Second World War, motivated by performance shortfalls and failures related to the operation of equipment used by humans.
• The studies showed that these problems could diminish when, engineering, psychology and physiology were considered when designing systems that would be handled by human beings.
• This definition shows that humans and their interaction with systems and devices should be considered during the design process. This need resulted in the proposal of an ISO Standard: BS EN ISO 13407 ”Human-centred design processes for interactive systems”.
• The interaction between humans and machines can be abstracted as illustrated in Figure 2.1. The machine receives inputs from its environment and provides information to the human operator through displays and other monitoring devices. The operator perceives the available information, process it and decides on his/her control actions. Based on the environment’s inputs and operator’s commands, the machine defines its outputs to the environment. • The machine receives inputs from its environment and provides information to the human operator through displays and other monitoring devices. The operator perceives the available information, process it and decides on his/her control actions. Based on the environment's inputs and operator's commands, the machine defines its outputs to the environment.
Humans handle devices, machines and equipment during their daily activities. All of these manipulations are susceptible to accidents or failures that can happen because of the interaction between operator, equipment and environment. Each interface with the operator can be a factor. For example:

## Slide 6
Introduction: Human Factors
Performance shortfalls and failures
Engineering, psychology and physiology
Notes: • Studies in the area of Human Factors started during the Second World War, motivated by performance shortfalls and failures related to the operation of equipment used by humans.
• The studies showed that these problems could diminish when, engineering, psychology and physiology were considered when designing systems that would be handled by human beings.
• This definition shows that humans and their interaction with systems and devices should be considered during the design process. This need resulted in the proposal of an ISO Standard: BS EN ISO 13407 ”Human-centred design processes for interactive systems”.
• The interaction between humans and machines can be abstracted as illustrated in Figure 2.1. The machine receives inputs from its environment and provides information to the human operator through displays and other monitoring devices. The operator perceives the available information, process it and decides on his/her control actions. Based on the environment’s inputs and operator’s commands, the machine defines its outputs to the environment. • The machine receives inputs from its environment and provides information to the human operator through displays and other monitoring devices. The operator perceives the available information, process it and decides on his/her control actions. Based on the environment's inputs and operator's commands, the machine defines its outputs to the environment.
Humans handle devices, machines and equipment during their daily activities. All of these manipulations are susceptible to accidents or failures that can happen because of the interaction between operator, equipment and environment. Each interface with the operator can be a factor. For example:

## Slide 7
Introduction: Human Factors
Performance shortfalls and failures
Engineering, psychology and physiology
Notes: • Studies in the area of Human Factors started during the Second World War, motivated by performance shortfalls and failures related to the operation of equipment used by humans.
• The studies showed that these problems could diminish when, engineering, psychology and physiology were considered when designing systems that would be handled by human beings.
• This definition shows that humans and their interaction with systems and devices should be considered during the design process. This need resulted in the proposal of an ISO Standard: BS EN ISO 13407 ”Human-centred design processes for interactive systems”.
• The interaction between humans and machines can be abstracted as illustrated in Figure 2.1. The machine receives inputs from its environment and provides information to the human operator through displays and other monitoring devices. The operator perceives the available information, process it and decides on his/her control actions. Based on the environment’s inputs and operator’s commands, the machine defines its outputs to the environment. • The machine receives inputs from its environment and provides information to the human operator through displays and other monitoring devices. The operator perceives the available information, process it and decides on his/her control actions. Based on the environment's inputs and operator's commands, the machine defines its outputs to the environment.
Humans handle devices, machines and equipment during their daily activities. All of these manipulations are susceptible to accidents or failures that can happen because of the interaction between operator, equipment and environment. Each interface with the operator can be a factor. For example:

## Slide 8
Introduction: Human Factors
Performance shortfalls and failures
Engineering, psychology and physiology
Notes: • Studies in the area of Human Factors started during the Second World War, motivated by performance shortfalls and failures related to the operation of equipment used by humans.
• The studies showed that these problems could diminish when, engineering, psychology and physiology were considered when designing systems that would be handled by human beings.
• This definition shows that humans and their interaction with systems and devices should be considered during the design process. This need resulted in the proposal of an ISO Standard: BS EN ISO 13407 ”Human-centred design processes for interactive systems”.
• The interaction between humans and machines can be abstracted as illustrated in Figure 2.1. The machine receives inputs from its environment and provides information to the human operator through displays and other monitoring devices. The operator perceives the available information, process it and decides on his/her control actions. Based on the environment’s inputs and operator’s commands, the machine defines its outputs to the environment. • The machine receives inputs from its environment and provides information to the human operator through displays and other monitoring devices. The operator perceives the available information, process it and decides on his/her control actions. Based on the environment's inputs and operator's commands, the machine defines its outputs to the environment.
Humans handle devices, machines and equipment during their daily activities. All of these manipulations are susceptible to accidents or failures that can happen because of the interaction between operator, equipment and environment. Each interface with the operator can be a factor. For example:

## Slide 9
Introduction: Mental Workload and Situation Awareness
Mental Workload
Situation Awareness
Notes: • Mental workload is one of the main concepts studied in Human Factors (STANTON et al., 2004).
• In order to explain it, Stanton et al. (2004) propose an analogy with the concept of physical workload. When an athlete must lift a dumbbell (one of those gym weights bars), the strength demand from the athlete is proportional to the dumbbell’s mass being lifted. If the dumbbell is lighter than the athlete’s capability, it is easy enough for him to lift it. If the athlete is strong enough to carry the dumbbell, he does not feel a physical demand bigger than his capabilities. In this case, the physical workload of this activity is appropriately fitted for this athlete. Two things can happen if the dumbbell is heavier than the athlete’s capability. Either the athlete adapts to lift the dumbbell using tools (adjust the strategy), or the dumbbell is not lifted completely (performance degrades). This situation corresponds to the case of a operator executing a task, which is not fitted for his capabilities.
• The mental workload is similar to the physical workload but refers to the mental capacity necessary to perform a task. Each human being has a finite mental capacity. When the mental demand is higher than the operator’s capacity, the person needs to adapt to finish the task, or the overall performance of the task is compromised. Otherwise, if the mental workload is too low, the operator may get bored and easily distracted and could also fail or not process the task’s information.
• It is important to say that mental workload is unique within each individual. It is influenced by the operator perception and also by other factors outside the task itself. These factor can be more related to the operator (like its skill, age, education, training) or the environment (like noise, heat and toxicity) (CAIN, 2007; FALLAHI et al., 2016; CARDOSO; GONTIJO, 2012).
• The mental workload is not a quantitative resource or something that one can directly measure, but several different methods have been proposed in the literature to infer it. Figure 2.2 illustrates three different classes of methods used to evaluate mental workload: methods based on task performance, methods based on physiological measures and methods based on subjective questionnaires.
Methods based on task performance • If the mental workload influences the task performance, it would be possible to infer it using the performance’s variation of a task. Because there are cases where the user’s mental capacity is too high for only one task, a common approach is to add a secondary task. In this case, the user is asked to maintain a good performance level and still try to execute both tasks. Both tasks should use the same skills (STANTON et al., 2004; SANDERS; MCCORMICK, 1998).
• For example, an experiment to assess mental workload in a flight simulator may use two tasks. The primary task is to fly the aircraft while maintaining a performance level. The second is something simple, like mentally summing two random numbers that appear on the screen. If the numbers’ sum is odd, the pilot should press the left arrow key on the keyboard, otherwise should press the right arrow key. If the pilot’s performance in the secondary task is too low, it means that the mental demand from the first task is too high to pay attention to the second task (MOHANAVELU et al., 2020).
Methods based on physiological measurements • Many physiological measurements can be used to assess mental workload. The most common ones are heart and brain activity (CHAKLADAR et al., 2020; ORLANDI; BROOKS, 2018), skin conductance, eye movement and pupillary contraction (STANTON et al., 2004; RODR´IGUEZ et al., 2015). These measurements are considered an unbiased assessment method (FALLAHI et al., 2016). It is recommended to evaluate them alongside another method, as they can be influenced by unknown variables and external factors.
• This work uses heart activity, obtained from an electrocardiogram (ECG) sensor, and electrodermal activity, obtained from a galvanic skin response (GSR) sensor, as physiological measurements to assess mental workload.
• The electrocardiogram (ECG) is a recording of the heart’s electrical activity. From it, it is possible to determine the intervals between heartbeats and the corresponding frequency (heart rate, HR). Another common variable is the heart rate standard deviation (heart rate variability, HRV) (CAIN, 2007). The heart activity is controlled by the sympathetic and parasympathetic nervous systems (STANTON et al., 2004). During a task, the heart activity changes with the mental demand of the task. The heart rate is expected to increase with the mental workload, while the heart rate variability is expected to decrease. These are consequences of two reactions in our system when in a mental demand situation (STANTON et al., 2004): a decrease in the parasympathetic nervous system activity and an increase in sympathetic nervous system activity. The ECG is a simple and non-invasive method used in many experiments to evaluate mental workload and other human factors’ (MOHANAVELU et al., 2020; MANSIKKA et al., 2016; ZHANG et al., 2014).
• The skin electrodermal activity is affected by the person’s sweating and the level of moisture in the environment. It can be used to reveal changes in our sympathetic system (NOURBAKHSH et al., 2012; SHI et al., 2007). It has been used in the literature as an assessment method for stress and arousal (NOURBAKHSH et al., 2012; STANTON et al., 2004; SHI et al., 2007), the usability of human-computer systems (SHI et al., 2007) and also mental workload (ZHANG et al., 2014; BORGHINI et al., 2014).
Methods based on subjective questionnaires • The use of subjective questionnaires to assess mental workload has been extensively discussed in the literature (SANDERS; MCCORMICK, 1998; STANTON et al., 2004). They are sensitive to perceived difficulty, automation, concurrent activities and demand for multiple resources. The questionnaires can be unidimensional, which are more straighforward but has only a general workload score.
• It is discussed if one should only use subjective measures to measure MWL (SANDERS; MCCORMICK, 1998; STANTON et al., 2004). They are sensitive to perceived difficulty, automation, concurrent activities and demand for multiple resources. These tests can be unidimensional, which are more straighforward but has only a general workload score (STANTON et al., 2004),or multidimensional. Examples of multidimensional questionnaires are the Subjective Workload Assessment Technique (SWAT) and the NASA Task Load Index (NASA-TLX). SWAT decomposes the mental in three dimensions: time load, mental effort load, and psychological stress. NASA-TLX, a questionnaire created by Hart e Staveland (1988), uses six dimensions, as described in Table 2.1. These questionnaires were proposed to evaluate only one task/activity. If the user has performed two tasks (a primary and secondary task), he/she should be oriented to answer about the primary task, not a combination of both (SANDERS; MCCORMICK, 1998).
• Finally, it is essential to highlight that, to have a comprehensive evaluation of the mental workload, not to choose only one method, but to combine methods from the three classes (task performance, physiological measurements and subjective questionnaires). Mental workload is multidimensional and can reflect partially or differently in each method (SANDERS; MCCORMICK, 1998).

## Slide 10
Introduction: Mental Workload and Situation Awareness
Mental Workload
Situation Awareness
Notes: • Mental workload is one of the main concepts studied in Human Factors (STANTON et al., 2004).
• In order to explain it, Stanton et al. (2004) propose an analogy with the concept of physical workload. When an athlete must lift a dumbbell (one of those gym weights bars), the strength demand from the athlete is proportional to the dumbbell’s mass being lifted. If the dumbbell is lighter than the athlete’s capability, it is easy enough for him to lift it. If the athlete is strong enough to carry the dumbbell, he does not feel a physical demand bigger than his capabilities. In this case, the physical workload of this activity is appropriately fitted for this athlete. Two things can happen if the dumbbell is heavier than the athlete’s capability. Either the athlete adapts to lift the dumbbell using tools (adjust the strategy), or the dumbbell is not lifted completely (performance degrades). This situation corresponds to the case of a operator executing a task, which is not fitted for his capabilities.
• The mental workload is similar to the physical workload but refers to the mental capacity necessary to perform a task. Each human being has a finite mental capacity. When the mental demand is higher than the operator’s capacity, the person needs to adapt to finish the task, or the overall performance of the task is compromised. Otherwise, if the mental workload is too low, the operator may get bored and easily distracted and could also fail or not process the task’s information.
• It is important to say that mental workload is unique within each individual. It is influenced by the operator perception and also by other factors outside the task itself. These factor can be more related to the operator (like its skill, age, education, training) or the environment (like noise, heat and toxicity) (CAIN, 2007; FALLAHI et al., 2016; CARDOSO; GONTIJO, 2012).
• The mental workload is not a quantitative resource or something that one can directly measure, but several different methods have been proposed in the literature to infer it. Figure 2.2 illustrates three different classes of methods used to evaluate mental workload: methods based on task performance, methods based on physiological measures and methods based on subjective questionnaires.
Methods based on task performance • If the mental workload influences the task performance, it would be possible to infer it using the performance’s variation of a task. Because there are cases where the user’s mental capacity is too high for only one task, a common approach is to add a secondary task. In this case, the user is asked to maintain a good performance level and still try to execute both tasks. Both tasks should use the same skills (STANTON et al., 2004; SANDERS; MCCORMICK, 1998).
• For example, an experiment to assess mental workload in a flight simulator may use two tasks. The primary task is to fly the aircraft while maintaining a performance level. The second is something simple, like mentally summing two random numbers that appear on the screen. If the numbers’ sum is odd, the pilot should press the left arrow key on the keyboard, otherwise should press the right arrow key. If the pilot’s performance in the secondary task is too low, it means that the mental demand from the first task is too high to pay attention to the second task (MOHANAVELU et al., 2020).
Methods based on physiological measurements • Many physiological measurements can be used to assess mental workload. The most common ones are heart and brain activity (CHAKLADAR et al., 2020; ORLANDI; BROOKS, 2018), skin conductance, eye movement and pupillary contraction (STANTON et al., 2004; RODR´IGUEZ et al., 2015). These measurements are considered an unbiased assessment method (FALLAHI et al., 2016). It is recommended to evaluate them alongside another method, as they can be influenced by unknown variables and external factors.
• This work uses heart activity, obtained from an electrocardiogram (ECG) sensor, and electrodermal activity, obtained from a galvanic skin response (GSR) sensor, as physiological measurements to assess mental workload.
• The electrocardiogram (ECG) is a recording of the heart’s electrical activity. From it, it is possible to determine the intervals between heartbeats and the corresponding frequency (heart rate, HR). Another common variable is the heart rate standard deviation (heart rate variability, HRV) (CAIN, 2007). The heart activity is controlled by the sympathetic and parasympathetic nervous systems (STANTON et al., 2004). During a task, the heart activity changes with the mental demand of the task. The heart rate is expected to increase with the mental workload, while the heart rate variability is expected to decrease. These are consequences of two reactions in our system when in a mental demand situation (STANTON et al., 2004): a decrease in the parasympathetic nervous system activity and an increase in sympathetic nervous system activity. The ECG is a simple and non-invasive method used in many experiments to evaluate mental workload and other human factors’ (MOHANAVELU et al., 2020; MANSIKKA et al., 2016; ZHANG et al., 2014).
• The skin electrodermal activity is affected by the person’s sweating and the level of moisture in the environment. It can be used to reveal changes in our sympathetic system (NOURBAKHSH et al., 2012; SHI et al., 2007). It has been used in the literature as an assessment method for stress and arousal (NOURBAKHSH et al., 2012; STANTON et al., 2004; SHI et al., 2007), the usability of human-computer systems (SHI et al., 2007) and also mental workload (ZHANG et al., 2014; BORGHINI et al., 2014).
Methods based on subjective questionnaires • The use of subjective questionnaires to assess mental workload has been extensively discussed in the literature (SANDERS; MCCORMICK, 1998; STANTON et al., 2004). They are sensitive to perceived difficulty, automation, concurrent activities and demand for multiple resources. The questionnaires can be unidimensional, which are more straighforward but has only a general workload score.
• It is discussed if one should only use subjective measures to measure MWL (SANDERS; MCCORMICK, 1998; STANTON et al., 2004). They are sensitive to perceived difficulty, automation, concurrent activities and demand for multiple resources. These tests can be unidimensional, which are more straighforward but has only a general workload score (STANTON et al., 2004),or multidimensional. Examples of multidimensional questionnaires are the Subjective Workload Assessment Technique (SWAT) and the NASA Task Load Index (NASA-TLX). SWAT decomposes the mental in three dimensions: time load, mental effort load, and psychological stress. NASA-TLX, a questionnaire created by Hart e Staveland (1988), uses six dimensions, as described in Table 2.1. These questionnaires were proposed to evaluate only one task/activity. If the user has performed two tasks (a primary and secondary task), he/she should be oriented to answer about the primary task, not a combination of both (SANDERS; MCCORMICK, 1998).
• Finally, it is essential to highlight that, to have a comprehensive evaluation of the mental workload, not to choose only one method, but to combine methods from the three classes (task performance, physiological measurements and subjective questionnaires). Mental workload is multidimensional and can reflect partially or differently in each method (SANDERS; MCCORMICK, 1998).

## Slide 11
Introduction: Mental Workload and Situation Awareness
Mental Workload
Situation Awareness
Notes: • Mental workload is one of the main concepts studied in Human Factors (STANTON et al., 2004).
• In order to explain it, Stanton et al. (2004) propose an analogy with the concept of physical workload. When an athlete must lift a dumbbell (one of those gym weights bars), the strength demand from the athlete is proportional to the dumbbell’s mass being lifted. If the dumbbell is lighter than the athlete’s capability, it is easy enough for him to lift it. If the athlete is strong enough to carry the dumbbell, he does not feel a physical demand bigger than his capabilities. In this case, the physical workload of this activity is appropriately fitted for this athlete. Two things can happen if the dumbbell is heavier than the athlete’s capability. Either the athlete adapts to lift the dumbbell using tools (adjust the strategy), or the dumbbell is not lifted completely (performance degrades). This situation corresponds to the case of a operator executing a task, which is not fitted for his capabilities.
• The mental workload is similar to the physical workload but refers to the mental capacity necessary to perform a task. Each human being has a finite mental capacity. When the mental demand is higher than the operator’s capacity, the person needs to adapt to finish the task, or the overall performance of the task is compromised. Otherwise, if the mental workload is too low, the operator may get bored and easily distracted and could also fail or not process the task’s information.
• It is important to say that mental workload is unique within each individual. It is influenced by the operator perception and also by other factors outside the task itself. These factor can be more related to the operator (like its skill, age, education, training) or the environment (like noise, heat and toxicity) (CAIN, 2007; FALLAHI et al., 2016; CARDOSO; GONTIJO, 2012).
• The mental workload is not a quantitative resource or something that one can directly measure, but several different methods have been proposed in the literature to infer it. Figure 2.2 illustrates three different classes of methods used to evaluate mental workload: methods based on task performance, methods based on physiological measures and methods based on subjective questionnaires.
Methods based on task performance • If the mental workload influences the task performance, it would be possible to infer it using the performance’s variation of a task. Because there are cases where the user’s mental capacity is too high for only one task, a common approach is to add a secondary task. In this case, the user is asked to maintain a good performance level and still try to execute both tasks. Both tasks should use the same skills (STANTON et al., 2004; SANDERS; MCCORMICK, 1998).
• For example, an experiment to assess mental workload in a flight simulator may use two tasks. The primary task is to fly the aircraft while maintaining a performance level. The second is something simple, like mentally summing two random numbers that appear on the screen. If the numbers’ sum is odd, the pilot should press the left arrow key on the keyboard, otherwise should press the right arrow key. If the pilot’s performance in the secondary task is too low, it means that the mental demand from the first task is too high to pay attention to the second task (MOHANAVELU et al., 2020).
Methods based on physiological measurements • Many physiological measurements can be used to assess mental workload. The most common ones are heart and brain activity (CHAKLADAR et al., 2020; ORLANDI; BROOKS, 2018), skin conductance, eye movement and pupillary contraction (STANTON et al., 2004; RODR´IGUEZ et al., 2015). These measurements are considered an unbiased assessment method (FALLAHI et al., 2016). It is recommended to evaluate them alongside another method, as they can be influenced by unknown variables and external factors.
• This work uses heart activity, obtained from an electrocardiogram (ECG) sensor, and electrodermal activity, obtained from a galvanic skin response (GSR) sensor, as physiological measurements to assess mental workload.
• The electrocardiogram (ECG) is a recording of the heart’s electrical activity. From it, it is possible to determine the intervals between heartbeats and the corresponding frequency (heart rate, HR). Another common variable is the heart rate standard deviation (heart rate variability, HRV) (CAIN, 2007). The heart activity is controlled by the sympathetic and parasympathetic nervous systems (STANTON et al., 2004). During a task, the heart activity changes with the mental demand of the task. The heart rate is expected to increase with the mental workload, while the heart rate variability is expected to decrease. These are consequences of two reactions in our system when in a mental demand situation (STANTON et al., 2004): a decrease in the parasympathetic nervous system activity and an increase in sympathetic nervous system activity. The ECG is a simple and non-invasive method used in many experiments to evaluate mental workload and other human factors’ (MOHANAVELU et al., 2020; MANSIKKA et al., 2016; ZHANG et al., 2014).
• The skin electrodermal activity is affected by the person’s sweating and the level of moisture in the environment. It can be used to reveal changes in our sympathetic system (NOURBAKHSH et al., 2012; SHI et al., 2007). It has been used in the literature as an assessment method for stress and arousal (NOURBAKHSH et al., 2012; STANTON et al., 2004; SHI et al., 2007), the usability of human-computer systems (SHI et al., 2007) and also mental workload (ZHANG et al., 2014; BORGHINI et al., 2014).
Methods based on subjective questionnaires • The use of subjective questionnaires to assess mental workload has been extensively discussed in the literature (SANDERS; MCCORMICK, 1998; STANTON et al., 2004). They are sensitive to perceived difficulty, automation, concurrent activities and demand for multiple resources. The questionnaires can be unidimensional, which are more straighforward but has only a general workload score.
• It is discussed if one should only use subjective measures to measure MWL (SANDERS; MCCORMICK, 1998; STANTON et al., 2004). They are sensitive to perceived difficulty, automation, concurrent activities and demand for multiple resources. These tests can be unidimensional, which are more straighforward but has only a general workload score (STANTON et al., 2004),or multidimensional. Examples of multidimensional questionnaires are the Subjective Workload Assessment Technique (SWAT) and the NASA Task Load Index (NASA-TLX). SWAT decomposes the mental in three dimensions: time load, mental effort load, and psychological stress. NASA-TLX, a questionnaire created by Hart e Staveland (1988), uses six dimensions, as described in Table 2.1. These questionnaires were proposed to evaluate only one task/activity. If the user has performed two tasks (a primary and secondary task), he/she should be oriented to answer about the primary task, not a combination of both (SANDERS; MCCORMICK, 1998).
• Finally, it is essential to highlight that, to have a comprehensive evaluation of the mental workload, not to choose only one method, but to combine methods from the three classes (task performance, physiological measurements and subjective questionnaires). Mental workload is multidimensional and can reflect partially or differently in each method (SANDERS; MCCORMICK, 1998).

## Slide 12
Introduction: Extended Reality (XR)
Notes: • Extended reality is a broad term that refers to all different ways of combining virtual and real entities in a human-machine interface system. It is usually decomposed into four classes (augmented reality, augmented virtuality, mixed reality, and virtual reality) that differ on the level of reality and virtuality involved in the interface system.
• Milgram e Kishino (1994) organized these classes and created the concept of the “virtuality continuum”, as illustrated in Figure, as illustrated in Figure 2.4. On the left, the real environment represents the cases where the stimuli are not produced by a computer or any other digital system. Along the path to the right, the environment starts to incorporate digital elements until it reaches the far right, where all the elements in the environment are virtual and have a digital origin (NIJHOLT; TRAUM, 2005; DOOLANI et al., 2020).

## Slide 13
Introduction: Extended Reality (XR)
Notes: • Extended reality is a broad term that refers to all different ways of combining virtual and real entities in a human-machine interface system. It is usually decomposed into four classes (augmented reality, augmented virtuality, mixed reality, and virtual reality) that differ on the level of reality and virtuality involved in the interface system.
• Milgram e Kishino (1994) organized these classes and created the concept of the “virtuality continuum”, as illustrated in Figure, as illustrated in Figure 2.4. On the left, the real environment represents the cases where the stimuli are not produced by a computer or any other digital system. Along the path to the right, the environment starts to incorporate digital elements until it reaches the far right, where all the elements in the environment are virtual and have a digital origin (NIJHOLT; TRAUM, 2005; DOOLANI et al., 2020).

## Slide 14
Introduction: Extended Reality (XR)
Notes: • Extended reality is a broad term that refers to all different ways of combining virtual and real entities in a human-machine interface system. It is usually decomposed into four classes (augmented reality, augmented virtuality, mixed reality, and virtual reality) that differ on the level of reality and virtuality involved in the interface system.
• Milgram e Kishino (1994) organized these classes and created the concept of the “virtuality continuum”, as illustrated in Figure, as illustrated in Figure 2.4. On the left, the real environment represents the cases where the stimuli are not produced by a computer or any other digital system. Along the path to the right, the environment starts to incorporate digital elements until it reaches the far right, where all the elements in the environment are virtual and have a digital origin (NIJHOLT; TRAUM, 2005; DOOLANI et al., 2020).

## Slide 15
Introduction: Extended Reality (XR)
Notes: • Extended reality is a broad term that refers to all different ways of combining virtual and real entities in a human-machine interface system. It is usually decomposed into four classes (augmented reality, augmented virtuality, mixed reality, and virtual reality) that differ on the level of reality and virtuality involved in the interface system.
• Milgram e Kishino (1994) organized these classes and created the concept of the “virtuality continuum”, as illustrated in Figure, as illustrated in Figure 2.4. On the left, the real environment represents the cases where the stimuli are not produced by a computer or any other digital system. Along the path to the right, the environment starts to incorporate digital elements until it reaches the far right, where all the elements in the environment are virtual and have a digital origin (NIJHOLT; TRAUM, 2005; DOOLANI et al., 2020).
• The extreme left means full reality, where the stimuli is not produced by any computer or any other digital system. Along the path to the right, the environment starts to have some digital elements until it reaches the far right, where all the environmental elements have a digital origin. The first step from the ”Real Environment” to ”Virtual Reality” is the augmented reality.
• In the augmented reality system, the user sees some digital elements that are laid over the real environment. without making the user lose his sense of presence in the real world. These elements can be text, images, video, etc. Augmented reality can be used to assist workers in manufacturing and assembly tasks, as well as training (DOOLANI et al., 2020; FARRELL, 2018; MA; CHOI, 2007).
• While the augmented reality brings digital elements to the real environment, the augmented virtuality creates an environment that could only exist digitally, such as a fantasy world from games or movies. This scenario is the background of some other activity that is being done by the user in the real environment. An example is to train a pilot in a virtual environment but with an accurate mock-up of the cockpit, which provides physical buttons and inceptors for the pilot to touch and hold (FARSHID et al., 2018). Another example is to play sports, such as tennis, golf or baseball, in a complete digital arena but using the actual equipment with a tracker.
• The mixed reality stays in between the real and virtual environments. Unlike augmented reality and augmented virtuality, in a mixed reality system the user can manipulate digital elements as if they were inside the real world (DOOLANI et al., 2020). One example is when a client from a furniture store uses mixed reality not only to see how the furniture fits inside his room, but he can also move it and change its color, size and shape before buying or even going to the shop.
• On the far right of the virtuality continuum, the virtual reality is when the user is the only non-digital element, everything else is digital, immersing the user in a virtual environment, but, of course, inside the physical limits of the real environment (MA; CHOI, 2007). If the feeling of presence inside that environment is well tailored, the user can momentarily forget about the real environment and act and react accordingly to the virtual environment (FARRELL, 2018).
• Virtual reality is a powerful tool that allows a user to be transported to a tridimensional environment that could be out of reach or that does not exist but is needed for testing or training reasons (MUJBER et al., 2004). Inside this virtual environment, the user can walk, look around and feel as if the environment was real (SALAH et al., 2019). Figure 2.5 shows the representations of each of these Extended Reality classes.

## Slide 16
Introduction: Extended Reality (XR)
No element produced by a digital system.
Notes: • The extreme left means full reality, where the stimuli is not produced by any computer or any other digital system. Along the path to the right, the environment starts to have some digital elements until it reaches the far right, where all the environmental elements have a digital origin. The first step from the ”Real Environment” to ”Virtual Reality” is the augmented reality.

## Slide 17
Introduction: Extended Reality (XR)
Notes: • The extreme left means full reality, where the stimuli is not produced by any computer or any other digital system. Along the path to the right, the environment starts to have some digital elements until it reaches the far right, where all the environmental elements have a digital origin. The first step from the ”Real Environment” to ”Virtual Reality” is the augmented reality.

## Slide 18
Introduction: Extended Reality (XR)
Some digital elements laid over the real environment.
The elements can not be manipulated
User do not lose the sense of presence.
Notes: • In the augmented reality system, the user sees some digital elements that are laid over the real environment. without making the user lose his sense of presence in the real world. These elements can be text, images, video, etc. Augmented reality can be used to assist workers in manufacturing and assembly tasks, as well as training (DOOLANI et al., 2020; FARRELL, 2018; MA; CHOI, 2007).

## Slide 19
Introduction: Extended Reality (XR)
Notes: • In the augmented reality system, the user sees some digital elements that are laid over the real environment. without making the user lose his sense of presence in the real world. These elements can be text, images, video, etc. Augmented reality can be used to assist workers in manufacturing and assembly tasks, as well as training (DOOLANI et al., 2020; FARRELL, 2018; MA; CHOI, 2007).

## Slide 20
Introduction: Extended Reality (XR)
Background environment made with digital elements.
The elements can be manipulated
User has a feeling of presence inside the virtual environment.
Notes: • While the augmented reality brings digital elements to the real environment, the augmented virtuality creates an environment that could only exist digitally, such as a fantasy world from games or movies. This scenario is the background of some other activity that is being done by the user in the real environment. An example is to train a pilot in a virtual environment but with an accurate mock-up of the cockpit, which provides physical buttons and inceptors for the pilot to touch and hold (FARSHID et al., 2018). Another example is to play sports, such as tennis, golf or baseball, in a complete digital arena but using the actual equipment with a tracker.

## Slide 21
Introduction: Extended Reality (XR)
Notes: • While the augmented reality brings digital elements to the real environment, the augmented virtuality creates an environment that could only exist digitally, such as a fantasy world from games or movies. This scenario is the background of some other activity that is being done by the user in the real environment. An example is to train a pilot in a virtual environment but with an accurate mock-up of the cockpit, which provides physical buttons and inceptors for the pilot to touch and hold (FARSHID et al., 2018). Another example is to play sports, such as tennis, golf or baseball, in a complete digital arena but using the actual equipment with a tracker.

## Slide 22
Introduction: Extended Reality (XR)
Some digital elements laid over the real environment.
The digital elements can be manipulated
User do not lose the sense of presence.
Notes: • The mixed reality stays in between the real and virtual environments. Unlike augmented reality and augmented virtuality, in a mixed reality system the user can manipulate digital elements as if they were inside the real world (DOOLANI et al., 2020). One example is when a client from a furniture store uses mixed reality not only to see how the furniture fits inside his room, but he can also move it and change its color, size and shape before buying or even going to the shop.

## Slide 23
Introduction: Extended Reality (XR)
Notes: • The mixed reality stays in between the real and virtual environments. Unlike augmented reality and augmented virtuality, in a mixed reality system the user can manipulate digital elements as if they were inside the real world (DOOLANI et al., 2020). One example is when a client from a furniture store uses mixed reality not only to see how the furniture fits inside his room, but he can also move it and change its color, size and shape before buying or even going to the shop.

## Slide 24
Introduction: Extended Reality (XR)
All elements are digital and can be manipulated.
User has a feeling of presence inside the virtual environment.
Notes: • On the far right of the virtuality continuum, the virtual reality is when the user is the only non-digital element, everything else is digital, immersing the user in a virtual environment, but, of course, inside the physical limits of the real environment (MA; CHOI, 2007). If the feeling of presence inside that environment is well tailored, the user can momentarily forget about the real environment and act and react accordingly to the virtual environment (FARRELL, 2018).

## Slide 25
Introduction: Extended Reality (XR)
Notes: • On the far right of the virtuality continuum, the virtual reality is when the user is the only non-digital element, everything else is digital, immersing the user in a virtual environment, but, of course, inside the physical limits of the real environment (MA; CHOI, 2007). If the feeling of presence inside that environment is well tailored, the user can momentarily forget about the real environment and act and react accordingly to the virtual environment (FARRELL, 2018).

## Slide 26
Introduction: Extended Reality (XR)
Notes: • Virtual reality is a powerful tool that allows a user to be transported to a tridimensional environment that could be out of reach or that does not exist but is needed for testing or training reasons (MUJBER et al., 2004). Inside this virtual environment, the user can walk, look around and feel as if the environment was real (SALAH et al., 2019). Figure 2.5 shows the representations of each of these Extended Reality classes.

## Slide 27
Introduction: Co-Design
Notes: • Co-design, or collaborative design, refers to a design process in which individuals of the design team have different backgrounds or bring different experiences, which can be essencial for the product under design. It is based on good communication and information sharing among the team (CHIU, 2002). Kleinsmann (2006) provides the following definition:.
”Collaborative design is the process in which actors from different disciplines share their knowledge about both the design process and the design content. They do that to create a shared understanding of both aspects, to be able to integrate and explore their knowledge and to achieve the larger common objective: the new product to be designed.” (KLEINSMANN, 2006).
• This definition emphasizes two critical aspects of co-design: knowledge sharing and integration. According to Kleinsmann (2006) knowledge is the data after the receiver’s understanding or translating process, in a state that is possible to record or register, so that the person can remember and use it later. During the collaborative design, ideas, facts or concepts are exchanged between the actors. This exchange is a fundamental part of the co-design method since it is responsible for the growth of each individual’s knowledge. Once the knowledge is shared among the actors, they can use it when performing their tasks, resulting in knowledge integration (KLEINSMANN, 2006).

## Slide 28
Conclusion and outlook
5.
Results and discussion
4.
Materials and Methods
3.
Objectives and Approach
2.
Introduction
1.
Agenda

## Slide 29
Introduction: Objectives
Research goals
Goal n° 1
  Compare:
    Assistive devices;
    Human factors;
    Virtual environment.
  Main Limitations
Goal n° 2
  non-BVI users:
    Deprived of their vision;
    Similarly assistive devices as BVI users.
Specific goals
Specific goal n° 1
Select a scenario and develop its virtual environment
Specific goal n° 2
Develop three conceptual assistive devices
Specific goal n° 3
Propose a set of evaluation methods
Specific goal n° 4
Design and execute an experiment

## Slide 30
Introduction: Approach

## Slide 31
Introduction: Approach

## Slide 32
Introduction: Approach
Notes: • Select a scenario for testing assistive devices and develop it in a virtual environment; • Develop three concepts of assistive devices that use different senses to provide input to the BVI; • Propose a set of methods for BVI to evaluate assistive devices from human factors perspective; • Design and execute an experiment to evaluate the concepts of assistive devices in the virtual environment using the proposed methods

## Slide 33
Conclusion and outlook
5.
Results and discussion
4.
Materials and Methods
3.
Objectives and Approach
2.
Introduction
1.
Agenda

## Slide 34
Conclusion and outlook
5.
Results and discussion
4.
Materials and Methods
3.
Objectives and Approach
2.
Introduction
1.
Agenda

## Slide 35
Conclusion and outlook
5.
Results and discussion
4.
Materials and Methods
3.
Objectives and Approach
2.
Introduction
1.
Agenda

## Slide 36
Thank You!
Ivan de Souza Rehder
ivan@ita.br / (55-12) 3947-5779
Acknowledgments

## Slide 37
Backup: New Agenda